## Slide 1: CORF: Coalescing Operand Register File for GPUs
Hodjat Asghari Esfeden
Farzad Khorasani
Daniel Wong
Hyeran Jeon
Nael Abu-Ghazaleh
The 24th International Conference on Architectural Support for Programming Languages and Operating Systems – ASPLOS 2019

## Slide 2: GPU Register File
Chart: Size (MB)
| Fermi (2010) | Kepler (2012) | Maxwell (2014) | Pascal (2016) | Volta (2018)
Register File | 2 | 3.8 | 6 | 14 | 20
L2 Cache | 0.75 | 1.5 | 3 | 4 | 6
Frequent accesses to the RF consume a substantial amount of the dynamic energy.
Port contention due to limited ports on operand collection stage affect performance as register operations are serialized.

## Slide 3: Our Proposal: CORF
Results:
RF dynamic energy by 17%
IPC by 9%
RF static energy by 52%
Idea: Combining multiple register reads into a single physical read

## Slide 4: Outline
‌Background and Motivation
CORF: Coalescing Operand Register File
  Compile Time Operation
  Run Time Operation
  Limitation
CORF++: Re-architected RF
  Compile Time Operation
  Run Time Operation
Evaluation
Summary

## Slide 5: Baseline Register File
Do all values need full 32-bit width to be represented?
GPU Register File Design
P0
P1
.
P255
Sub-bank 0
.
.
t0
t1
t2
t3
Sub-bank 1
t4
t5
t6
t7
.
.
.
Sub-bank 7
t28
t29
t30
t31
128-bits
128 KB RF per SM
  Split across 4 banks
  A bank is made up of 8 sub-banks, each 128 bits wide
  A full warp register can be striped using one entry of one bank
Bank 0
32-bits
GPU Register File Design

## Slide 6: Prominence of Narrow-width Values
Register operand characteristic
Chart: Percentage
| BFS | BTREE | GUASSIAN | MUM | NW | SRAD | SAD | VECTORADD | REDUCTION | BACKPROB | HEARTWALL | STO | AlexNet[CNN] | SqueezeNet[CNN] | CifarNet[CNN] | GRU[RNN] | AVG | LIB | SGEMM | BLACHSCHOLES | WP | AVG | AVG
1-byte | 0.33719 | 0.45419 | 0.72329 | 0.69987 | 0.47178 | 0.28152 | 0.63934 | 0.096638 | 0.24393 | 0.65733 | 0.19113 | 0.20578 | 0.55377 | 0.61656 | 0.62946 | 0.039482 | 0.42758 | 0.12596 | 0.09124 | 0.000432 | 0.10885 | 0.08162 | 0.35839
2-bytes | 0.46527 | 0.23037 | 0.089606 | 0.024665 | 0.1233 | 0.15887 | 0.11196 | 0.211 | 0.17233 | 0.17892 | 0.57443 | 0.090571 | 0.21246 | 0.21236 | 0.20638 | 0.35415 | 0.21354 | 0.24107 | 0.11434 | 0.088197 | 0.32162 | 0.19131 | 0.20909
3-bytes | 0.0023505 | 0.099443 | 0.04085 | 0.11426 | 0.095159 | 0.2197 | 0.008329 | 0.15538 | 0.34139 | 0.019374 | 0.029702 | 0.01198 | 0.071629 | 0.046548 | 0.015381 | 0.045964 | 0.08234 | 0.17168 | 0.14932 | 0.21284 | 0.13637 | 0.16755 | 0.099383
4-bytes | 0.19519 | 0.216 | 0.14626 | 0.1612 | 0.30976 | 0.33992 | 0.24037 | 0.53698 | 0.24235 | 0.14438 | 0.20474 | 0.69167 | 0.16214 | 0.12454 | 0.14879 | 0.56041 | 0.27654 | 0.4613 | 0.6451 | 0.69853 | 0.43315 | 0.55952 | 0.33314
72%
33%
65%
Can we pack multiple narrow-width values into a single physical register?

## Slide 7: Register Packing
Packed RF
Co-locating multiple narrow-width registers in the same physical register [Ergin’04][Wang’17]
r1
r5
r2
r3
r4
Baseline RF
Can we combine multiple register reads required by an instruction?
Goal of register packing is to
  First fit policy is used at the allocation time
  Mapping is done using a Renaming Table logic
But, still each register read requires a separate physical register read
P1
P2
P3
P4
P5
P1
P2
P3
P4
P5
r1
r5
r2
r3
r4
r1
r5
r2
r3
r4
reduce the effective size of register file
40% saving!

## Slide 8: Coalescing Opportunities
Let’s try to coalesce reads using simple register packing (with first fit policy)
Upper bound: Fraction of all dynamic instructions which:
  Contain two register source operands that are both narrow-width
  They fit together in a single register entry
First fit is weak in promoting coalescing; how to pack the right registers together?
Chart: Percentage
| BFS | BTREE | GUASSIAN | MUM | NW | SRAD | SAD | VECTORADD | REDUCTION | BACKPROB | HEARTWALL | STO | AlexNet[CNN] | SqueezeNet[CNN] | CifarNet[CNN] | GRU[RNN] | AVG | LIB | SGEMM | BLACHSCHOLES | WP | AVG | AVG
First-fit | 0.068422 | 0.076415 | 0.065843 | 0.04395 | 0.061365 | 0.046598 | 0.028655 | 0.12355 | 0.079526 | 0.031547 | 0.026542 | 0.063695 | 0.086495 | 0.063216 | 0.039852 | 0.018542 | 0.057763 | 0.018691 | 0.012694 | 0.026312 | 0.014965 | 0.018166 | 0.049844
Upper bound | 0.5862 | 0.73539 | 0.89094 | 0.63715 | 0.85099 | 0.67167 | 0.9137 | 0.62534 | 0.71925 | 0.86482 | 0.89284 | 0.66275 | 0.76195 | 0.8147 | 0.70464 | 0.56615 | 0.74366 | 0.51575 | 0.39666 | 0.54182 | 0.49472 | 0.48724 | 0.69237
Let’s incorporate a compiler-guided register allocation policy to identify pairs of registers commonly read together
Instructions with coalesce-able register reads
69%
4%

## Slide 9: CORF: Overview
Register pairs are identified at compile time through static analysis.
  (r1, r3) as well as (r2, r4).
At run-time, common register pairs will be dynamically packed together, if possible.
  (r2, r4) in this example.
(r1, r3)
r1, r2 (r2, r4) r1, r4
Kernel Binary
Compile time
Execution time
Profile Register Pairings
Common Pairs Identification
CORF RF
10
8
7
2
r2
r1
r4
r3
r4
----
r3
r2
----
r1

## Slide 10: CORF: Compile Time Operation
Identifying exclusive common pairs
  Profiling the frequency of register pairs in order
  to build a Register Affinity Graph
  Remove edges of the registers that have more than
  one edge to identify exclusive common pairs
Passing compiler-assisted helps to the hardware
  Set of exclusive register pairs identified by the compiler are annotated in the executable’s preamble of a kernel
(r1, r3)
r1, r2 (r2, r4) r1, r4
Compile time
Profile Register Pairings
Common Pairs Identification
10
8
7
2
r2
r1
r4
r3

## Slide 11: CORF: Run Time Operation
During run time, CORF packs the identified register pairs into
the same physical register entry
  (r1, r3) do not fit in a single physical register
Coalescing opportunities are identified using the Renaming Table
  If the two source operands reside in the same physical register, then accesses are coalesced
CORF coalescing opportunities are limited to registers stored within the same physical register entry.
Execution time
CORF RF
r4
----
r3
r2
----
r1
What if a register is commonly accessed with two or more other registers?

## Slide 12: CORF++: Overview
Instead of identifying exclusive register pairs, compiler solves a variant of graph coloring problem to simplify the allocation to left or right-aligning assignment
During runtime, any left-aligned register is coalesce-able with any right-aligned register providing they don't overlap.
Kernel Binary
Compile time
Execution time
Register Affinity Graph
Alignment Identification
Coalescing-Aware RF
r2
----
r4
----
r1
r5
r6
r3
Left
r1
r4
Right
r2
r3
r5
r6
How to architect the RF to allow coalescing across different phys. registers?
How to allocate registers to left/right RF slices for maximizing coalescing opportunities?

## Slide 13: CORF++: Compiler Support
Optimal solution to remove the minimum number of edges of a graph to make it two-colorable is NP-hard
Any graph with no odd cycles (cycles made up of an odd number of edges) is 2-colorable
We developed the following heuristic to remove all odd cycles:
    Assign each edge a weight corresponding to its original weight, divided by the number of odd cycles that removing it would break
    Remove the edge with the minimum weight and update the weights
    Repeat until all odd cycles are eliminated

## Slide 14: CORF++: Architecture Support
To support coalescing across different physical register entries, we need dual-addressable banks
Moreover, we need to changed register-to-bank mapping policy
  Details in the paper
Subbank 0
Subbank 1
Subbank 2
Subbank 3
Subbank 4
Subbank 5
Subbank 6
Subbank 7
MUX
MUX
MUX
MUX
MUX
MUX
MUX
MUX
Address 1: P2
Address 2: P3
Execution time
Coalescing-Aware RF
r2
----
r4
----
r1
r5
r6
r3
P2
P3

## Slide 15: Coalesced Instructions
CORF and CORF++ significantly increase the amount of coalescing opportunity
Chart: Percentage
| BFS | BTREE | GUASSIAN | MUM | NW | SRAD | SAD | VECTORADD | REDUCTION | BACKPROB | HEARTWALL | STO | AlexNet[CNN] | SqueezeNet[CNN] | CifarNet[CNN] | GRU[RNN] | AVG | LIB | SGEMM | BLACHSCHOLES | WP | AVG | AVG
First-fit | 0.068422 | 0.076415 | 0.065843 | 0.04395 | 0.061365 | 0.046598 | 0.028655 | 0.12355 | 0.079526 | 0.031547 | 0.026542 | 0.063695 | 0.086495 | 0.063216 | 0.039852 | 0.018542 | 0.057763 | 0.018691 | 0.012694 | 0.026312 | 0.014965 | 0.018166 | 0.049844
CORF | 0.21564 | 0.23182 | 0.34804 | 0.17866 | 0.37637 | 0.18547 | 0.19887 | 0.21325 | 0.24527 | 0.23943 | 0.2267 | 0.31261 | 0.29875 | 0.29465 | 0.32129 | 0.22558 | 0.25703 | 0.079035 | 0.12506 | 0.13606 | 0.12248 | 0.11566 | 0.22875
CORF++ | 0.29547 | 0.61295 | 0.58521 | 0.48251 | 0.68542 | 0.59642 | 0.60254 | 0.21325 | 0.62523 | 0.59452 | 0.63843 | 0.56251 | 0.69235 | 0.62574 | 0.55232 | 0.30564 | 0.54191 | 0.27123 | 0.19542 | 0.28137 | 0.23423 | 0.24556 | 0.48264
Upper Bound | 0.5862 | 0.73539 | 0.89094 | 0.63715 | 0.85099 | 0.67167 | 0.9137 | 0.62534 | 0.71925 | 0.86482 | 0.89284 | 0.66275 | 0.76195 | 0.8147 | 0.70464 | 0.56615 | 0.74366 | 0.51575 | 0.39666 | 0.54182 | 0.49472 | 0.48724 | 0.69237
FP-intensive
INT-intensive
69%
4%
23%
48%
Fraction of coalesced instructions

## Slide 16: Performance Improvement
Chart: Percentage
| BFS | BTREE | GUASSIAN | MUM | NW | SRAD | SAD | VECTORADD | REDUCTION | BACKPROB | HEARTWALL | STO | AlexNet[CNN] | SqueezeNet[CNN] | CifarNet[CNN] | GRU[RNN] | AVG | LIB | SGEMM | BLACHSCHOLES | WP | AVG | AVG
CORF | 0.03594 | 0.049538 | 0.050294 | 0.021864 | 0.051348 | 0.04392 | 0.025975 | 0.029834 | 0.04843 | 0.059746 | 0.034922 | 0.06697 | 0.075862 | 0.069694 | 0.054678 | 0.049235 | 0.048016 | 0.014683 | 0.025146 | 0.019642 | 0.0084615 | 0.016983 | 0.041809
CORF++ | 0.044174 | 0.13098 | 0.084567 | 0.05905 | 0.093512 | 0.14124 | 0.078699 | 0.029834 | 0.12346 | 0.14835 | 0.098345 | 0.10871 | 0.17581 | 0.18334 | 0.093996 | 0.06671 | 0.1038 | 0.05039 | 0.039293 | 0.040619 | 0.016183 | 0.036621 | 0.090363
FP-intensive
INT-intensive
CORF and CORF++ improve IPC by reducing the pressure on RF ports
4%
9%
IPC improvement

## Slide 17: RF Access Reduction—Dynamic Energy
Chart: Percentage
| BFS | BTREE | GUASSIAN | MUM | NW | SRAD | SAD | VECTORADD | REDUCTION | BACKPROB | HEARTWALL | STO | AlexNet[CNN] | SqueezeNet[CNN] | CifarNet[CNN] | GRU[RNN] | AVG | LIB | SGEMM | BLACHSCHOLES | WP | AVG | AVG
CORF | 0.088858 | 0.12546 | 0.19854 | 0.072966 | 0.15199 | 0.084706 | 0.084182 | 0.075747 | 0.10291 | 0.12685 | 0.10813 | 0.16295 | 0.1427 | 0.1265 | 0.15642 | 0.08632 | 0.11845 | 0.035973 | 0.048267 | 0.054892 | 0.039436 | 0.044642 | 0.10369
CORF++ | 0.10374 | 0.33172 | 0.29296 | 0.19706 | 0.32468 | 0.34347 | 0.27265 | 0.075747 | 0.29818 | 0.31255 | 0.30452 | 0.26451 | 0.36132 | 0.30127 | 0.29412 | 0.12345 | 0.26262 | 0.12345 | 0.075421 | 0.11351 | 0.075421 | 0.096953 | 0.22949
CORF and CORF++ reduce RF accesses which gets translated to 8.5% and 17% dynamic energy reduction
10%
23%
Register file access reduction

## Slide 18: Effective Size of RF—Static Energy
Reduction in effective size of RF gets translated to 53% static energy reduction
Chart: Percentage
| BFS | BTREE | GUASSIAN | MUM | NW | SRAD | SAD | VECTORADD | REDUCTION | BACKPROB | HEARTWALL | STO | AlexNet[CNN] | SqueezeNet[CNN] | CifarNet[CNN] | GRU[RNN] | AVG | LIB | SGEMM | BLACHSCHOLES | WP | AVG | AVG
CORF++ | 0.19272 | 0.41447 | 0.58845 | 0.30759 | 0.33967 | 0.31598 | 0.48417 | 0.23981 | 0.33052 | 0.56411 | 0.41547 | 0.2088 | 0.51689 | 0.49689 | 0.51641 | 0.21467 | 0.38416 | 0.26398 | 0.1517 | 0.12386 | 0.19765 | 0.34419 | 0.32118
RF-Virtualization | 0.30388 | 0.29637 | 0.79948 | 0.53005 | 0.35828 | 0.22231 | 0.54062 | 0.49048 | 0.33958 | 0.38799 | 0.22892 | 0.20108 | 0.36945 | 0.58762 | 0.63245 | 0.20077 | 0.40558 | 0.17943 | 0.12312 | 0.40776 | 0.19858 | 0.36991 | 0.3505
Combined | 0.44413 | 0.58373 | 0.90273 | 0.65431 | 0.57465 | 0.46805 | 0.76246 | 0.61267 | 0.55786 | 0.73323 | 0.54928 | 0.3679 | 0.69538 | 0.79253 | 0.82225 | 0.37234 | 0.61834 | 0.39604 | 0.25614 | 0.48112 | 0.35698 | 0.56919 | 0.54383
Register file size reduction
34%
35%
54%

## Slide 19: Summary
Register file is a critical structure in GPUs
A lot of values do not require full-width register to be represented
We proposed CORF which combines multiple register reads into a single physical register read
CORF++ furtherly re-architects RF to take more advantage of register coalescing opportunities
Our technique improves IPC by 9% and reduces RF dynamic and static energy by 17% and 52%, respectively.

## Slide 20: CORF: Coalescing Operand Register File for GPUs
Hodjat Asghari Esfeden
Farzad Khorasani
Daniel Wong
Hyeran Jeon
Nael Abu-Ghazaleh
The 24th International Conference on Architectural Support for Programming Languages and Operating Systems – ASPLOS 2019

## Slide 21: RF Dynamic Energy
Chart: Percentage
| BFS | BTREE | GUASSIAN | MUM | NW | SRAD | SAD | VECTORADD | REDUCTION | BACKPROB | HEARTWALL | STO | AlexNet[CNN] | SqueezeNet[CNN] | CifarNet[CNN] | GRU[RNN] | AVG | LIB | SGEMM | BLACHSCHOLES | WP | AVG | AVG
Dynamic Energy | 0.91114 | 0.87454 | 0.80146 | 0.92703 | 0.84801 | 0.91529 | 0.91582 | 0.46213 | 0.89709 | 0.87315 | 0.89187 | 0.83705 | 0.85612 | 0.86796 | 0.84597 | 0.91589 | 0.85253 | 0.96403 | 0.95173 | 0.94511 | 0.96056 | 0.95389 | 0.8731
Overhead Dynamic Energy | 0.018473 | 0.064049 | 0.040654 | 0.04178 | 0.023287 | 0.043536 | 0.063524 | 0.035767 | 0.043536 | 0.064338 | 0.069168 | 0.067961 | 0.018473 | 0.023287 | 0.035767 | 0.018473 | 0.042005 | 0.021768 | 0.024375 | 0.021768 | 0.021774 | 0.022389 | 0.042442
Chart: Percentage
| BFS | BTREE | GUASSIAN | MUM | NW | SRAD | SAD | VECTORADD | REDUCTION | BACKPROB | HEARTWALL | STO | AlexNet[CNN] | SqueezeNet[CNN] | CifarNet[CNN] | GRU[RNN] | AVG | LIB | SGEMM | BLACHSCHOLES | WP | AVG | AVG
Dynamic Energy | 0.89626 | 0.65828 | 0.70704 | 0.84294 | 0.76928 | 0.80874 | 0.72886 | 0.46213 | 0.78182 | 0.71624 | 0.78173 | 0.76881 | 0.7647 | 0.80266 | 0.74986 | 0.8927 | 0.75825 | 0.90379 | 0.94448 | 0.90536 | 0.93745 | 0.92277 | 0.79115
Overhead Dynamic Energy | 0.018473 | 0.064049 | 0.040654 | 0.04178 | 0.023287 | 0.043536 | 0.063524 | 0.035767 | 0.043536 | 0.064338 | 0.069168 | 0.067961 | 0.018473 | 0.035767 | 0.043536 | 0.018473 | 0.044755 | 0.021768 | 0.024375 | 0.021768 | 0.021774 | 0.022167 | 0.043225

## Slide 22: RF Static Energy
Chart: Percentage
| BFS | BTREE | GUASSIAN | MUM | NW | SRAD | SAD | VECTORADD | REDUCTION | BACKPROB | HEARTWALL | STO | AlexNet[CNN] | SqueezeNet[CNN] | CifarNet[CNN] | GRU[RNN] | AVG | LIB | SGEMM | BLACHSCHOLES | WP | AVG | AVG
Static Energy | 0.7763 | 0.52136 | 0.38047 | 0.66509 | 0.61645 | 0.62231 | 0.48096 | 0.73817 | 0.61237 | 0.38577 | 0.54769 | 0.72254 | 0.47709 | 0.51681 | 0.54666 | 0.77812 | 0.58676 | 0.70821 | 0.82445 | 0.84744 | 0.79172 | 0.79281 | 0.628
Overhead Static Energy | 0.059672 | 0.055253 | 0.057368 | 0.059606 | 0.05793 | 0.056455 | 0.057859 | 0.060256 | 0.05676 | 0.054917 | 0.058143 | 0.056669 | 0.057368 | 0.059606 | 0.05793 | 0.056455 | 0.057564 | 0.059709 | 0.060309 | 0.060021 | 0.061232 | 0.060312 | 0.058227
FP-intensive
INT-intensive
Chart: Percentage
| BFS | BTREE | GUASSIAN | MUM | NW | SRAD | SAD | VECTORADD | REDUCTION | BACKPROB | HEARTWALL | STO | AlexNet[CNN] | SqueezeNet[CNN] | CifarNet[CNN] | GRU[RNN] | AVG | LIB | SGEMM | BLACHSCHOLES | WP | AVG | AVG
Static Energy | 0.53453 | 0.37065 | 0.089926 | 0.33205 | 0.39708 | 0.48396 | 0.22149 | 0.37611 | 0.40442 | 0.23609 | 0.42232 | 0.57725 | 0.27784 | 0.19062 | 0.15734 | 0.60785 | 0.35497 | 0.58114 | 0.72295 | 0.50189 | 0.6345 | 0.60982 | 0.406
Overhead Static Energy | 0.059672 | 0.055253 | 0.057368 | 0.059606 | 0.05793 | 0.056455 | 0.057859 | 0.060256 | 0.05676 | 0.054917 | 0.058143 | 0.056669 | 0.05676 | 0.054917 | 0.058143 | 0.056669 | 0.057564 | 0.059709 | 0.060309 | 0.060021 | 0.061232 | 0.060312 | 0.058227
FP-intensive
INT-intensive

## Slide 23: Methodology
Simulator:
  GPGPU-Sim modeling NVIDIA Fermi architecture
Workloads:
  Rodinia
  Parboil
  CUDA-SDK
  Tango
Notes: I need to put more stuff here… A lot of white space…

## Slide 24: CORF++: Illustrative Example
r4
r4
GLD r1, [0x80];
ISUB r2, r1, 0x7;
SHR r4, r1, 0x8;
LLD r3, [r4];
IADD r5, r2, r3;
IMUL r1, r4, r5;
ISUB r2, r3, r4;
SASS Code:
A
B
<L: r3, r5 | R: r2, r4>
GLD r1, [0x80];
ISUB r2, r1, 0x7;
Physical
Register
File
P0
P1
P2
r1
r2
Physical
Register
File
P0
P1
P2
r1
r2
SHR r4, r1, 0x8;
C
<L: r3, r5 | R: r2, r4>
D
<L: r3, r5 | R: r2, r4>
E
<L: r3, r5 | R: r2, r4>
LLD r3, [r4];
IADD r5, r2, r3;
Physical
Register
File
P0
P1
P2
r1
r2
r3
Physical
Register
File
P0
P1
P2
r1
r2
r4
r3
r5
F
<L: r3, r5 | R: r2, r4>
IMUL r1, r4, r5;
ISUB r2, r3, r4
Physical
Register
File
P0
P1
P2
r1
r2
r4
r3
r5